## Slide 1: Traffic sign recognition – CNN on microcontrollers
Machine Learning on Microcontroller Course – 2020 ETH Zuerich

## Slide 2: Overview
Dataset introduction, challenges
Model selection
Metrics evaluation
Power evaluation
Demo

## Slide 3: The dataset
The dataset chosen is the German Traffic Sign Recognition Benchmark (GTSRB)
Released for a CV competition in 2011, teams used both handcrafted features and neural network (latter used as benchmark) [1]
Some remarks:
The images contain one traffic sign each
Image sizes vary between 15x15 to 250x250 pixels
Images are not necessarily squared
The actual traffic sign is not necessarily centered within the image.
Sample images

## Slide 4: Challenges and class imbalance
Challenges in traffic sign recognition (to name a few):
  viewpoint variations
  lighting conditions
  motion-blur
  sun glare
  physical damage
43 classes lead to pretty big networks, representing a challenging implementation on uC
Dataset was very umbalanced, with classes in the order 1:10.

## Slide 5: How class imbalance was handled
Possible augmentation strategies:
  Affine tranform
    -> Translation, rotation, scaling and shear somehow already present in the dataset (photos are taken from video of a running car)
  Random cutting the images
    -> Might cut important part of a signal (as first digit in speed limits)
  Photometric distortions
    -> Probably the best solution for traffic signs due to variable time of day and weather conditions. Endorsed by GoogLeNet [2][3]
    -> Chosen gamma correction to target exposure differences aforhead mentioned [4]

## Slide 6: Overview
Dataset introduction, challenges
Model selection
Metrics evaluation
Power evaluation
Demo

## Slide 7: Starting from paper SOA model…
SOA Neural Net model from the GTSRB competition: SermaNet [5]
Pro:
Extremely high accuracy, almost perfect score (98.97%) over a test set of 12600 traffic signs
Cons:
Way too much ROM/RAM (8MB/400kB) needed for a microcontroller implementation
Inference time would be very slow.

## Slide 8: … creating a new model, trade off memory and accuracy
How to find a smaller model?
Things done:
Resized the images, from 48*48 to 32*32 (size empirically found as sweet spot)
Grayscaled the images
Reduced number of convolutional filters and dense neurons
->… But how could I find the best?

## Slide 9: I trained more than 1000 models!
Insert meme drake here
About 1 month
About 2 days

## Slide 10: Parameters taken into consideration
I searched over the best among:
Number of layers and filters of convolutional
Number of neurons of the dense.
  ->They shown the biggest impact on memory and performance
Radius of the ball is the ROM occupancy, computed with a simple mathematical model of the neural net at validation time

## Slide 11: Best 100 models for validation loss
Picked the model with the lower validation loss that could fit on the microcontroller
[Byte]
Used early stopping
to find the right number of epoch and not overfit the models

## Slide 12: Model selected - GiordyNet
Model number
Validation accuracy
10xConv
50xConv
100xConv
100xDense
43xDense
MaxPooling (2x2),
BatchNorm,
ReLU
MaxPooling (2x2),
BatchNorm,
ReLU
MaxPooling (2x2),
BatchNorm,
ReLU
ReLU
Softmax
26*26
Input:
32*32
10*10
2*2

## Slide 13: Confusion matrix – SermaNet vs GiordyNet
Accuracy on testset: 98.97 Accuracy on testset: 94.7
ROM/RAM: 8MB/400kB ROM/RAM: 410kB/12kB
MAC: 249,275,645 MAC: 1,496,845
0.04x
19.5x/36.36x
166.5x

## Slide 14: Overview
Dataset introduction, challenges
Model selection
Metrics evaluation
Power evaluation
Demo

## Slide 15: Frameworks used – Comparison ahead
NNoM
Not batch normalized
Batch normalized
  Non compressed
  x4 compression
  x8 compression
Quantization aware
  16bit floating point
  Weights and activation quantized 8bit
Post-training quantization
  16bit floating point
  Weights quantized 8bit
  Weights and activation functions quantized 8bit, fixed point
8bit quantization, fixed point
  With CMSIS-NN backend
  W/o CMSIS-NN backend
CubeAI
Backend
NNoM
Backend

## Slide 16: Accuracy
Remarks:
all models has been tested on PC
Quantization aware is not supported in CubeAI yet, as 16bit floating point, so I tested only on PC
  In GCC FP16 are store variable only, so has to be casted to FP32 for computation
-w suffix means only weights are quantized, -wa means both weights and activation functions
Quant aware
Post-training quant
Percentage

## Slide 17: Speed performance – MAC Operations, comparison with SOA

## Slide 18: Speed performance – MAC Operations

## Slide 19: Speed performance – MAC Operations
I also tried with different compiler optimizations settings, and the only notable difference was with NNoM without the CMSIS-NN backend:
CMSIS-backed implementation with o-fast option between 1e-3 and 1e-4 relative difference than o-none
“Pure math” implementation with o-fast option: about 5.5x less cycles required than o-none
Please also note that in every test the hardware floating point implementation was activated:
-mfloat-abi=hard

## Slide 20: Speed performance – Cycles (and MAC)
 | STM32F7 | STM32F4
FP32 Op | 6 | 10.4
Int8 Op | 0.23 | 0.26
Average cycle/MAC_op:
My bet: SIMD instructions

## Slide 21: Memory usage – ROM, comparison with SOA
kBytes

## Slide 22: Memory usage – ROM
We can observe how CubeAI compression affects only dense layers
The biggest model is less than half of the ROM available on STM32L4, and the smallest one is near 10% of memory occupation
kBytes

## Slide 23: Memory usage – RAM, comparison with SOA
[kBytes]

## Slide 24: Memory usage – RAM
Ram usage is rather good,
it uses around 10% of RAM available on STM32L4
[kBytes]

## Slide 25: Inference time – F7

## Slide 26: Inference time – F4
CMSIS-NN

## Slide 27: Summary – Precision/ROM
CMSIS-NN
Best tradeoff model highlighted in yellow
Percentage
[kBytes]

## Slide 28: Summary table of all metrics – Highlighted the best model
Quant/Not quant | Implementation | Test | Backend | Accuracy PC [%] | Accuracy uC [%] | MAC | Cycle | Time for inference | ROM [kB] | RAM [kB]
Non quant | PC | SOA model | Keras | 98,97 | - | 249275645 | - | - | 8112 | 426
Non quant | PC/uC-CubeAI | Keras w/o bn | Keras | 93,63 | 93,63 | 1490765 | 15605249 | 195,0656125 | 412,37 | 11,96
Non quant | PC/uC-CubeAI | Keras | Keras | 94,19 | 94,19 | 1496845 | 15655240 | 195,6905 | 413,65 | 11,96
Non quant | PC/uC-CubeAI | Keras – compress x4 | Keras | 94,19 | 91,89 | 1496845 | 15664381 | 195,8047625 | 371,52 | 11,96
Non quant | PC/uC-CubeAI | Keras – compress x8 | Keras | 94,19 | 90,79 | 1496845 | 15710674 | 196,383425 | 362,45 | 11,96
Quant aware | PC | TFLite - fp16 | TFLite | 93 | - | - | - | - | 213,78 | -
Quant aware | PC | TFLite - int8 | TFLite | 82,4 | - | - | - | - | 104,81 | -
Post train quant | PC | TFLite - fp16 - w | TFLite | 92,5 | - | - | - | - | 213,78 | -
Post train quant | PC/uC-CubeAI(demo) | TFLite - int8 - w | TFLite | 91,9 | 90,71 | 1469917 | 8022150 | 100,276875 | 104,81 | 13,52
Post train quant | PC/uC-CubeAI | TFLite - int8 - wa | TFLite | 72,3 | 66,87 | 1498879 | 8064758 | 100,809475 | 104,81 | 13,52
Post train quant | PC/uC-NNoM | NNoM | Keras - NNoM | 66,77 | 66,77 | 1465300 | 126951572 | 1586,89465 | 103,5 | 11,6
Post train quant | PC/uC-NNoM (demo) | NNoM - CMSIS-NN | Keras - NNoM | 66,77 | 66,77 | 1465300 | 7293643 | 91,1705375 | 103,5 | 11,6

## Slide 29: Overview
Dataset introduction, challenges
Model selection
Metrics evaluation
Power evaluation
Demo

## Slide 30: Testbench
Unfortunately I do not have a power meter at home, so I built one!
It is a shunt ammeter featuring an Arduino and an instrumental amplifier made with three UA741

## Slide 31: Testbench
Using three opamps to decouple impedences from the shunt resistor and amplyfing so I could put a low resistor (1.8ohm) and have a low burden voltage (less than 0.2V)

## Slide 32: Testbench
After researching on the schematic provided by ST for the Nucleo board I could only spot the header that powers the entire board, sensors included.
To not poison the results I have measured the current consumption of the board putting the uC in sleep mode and so offsetting the further readings
Credits: ST Electronics

## Slide 33: Testbench

## Slide 34: Testbench

## Slide 35: Testbench

## Slide 36: Summary on power consumption – Tensorflow int8-w
Freq | Current-F4 | Current-F7 | Power-F4 | Power-F7 | Energy/inference F4 | Energy/inference F7
216MHz | - | 90mA | - | 300mW | - | 12mJ
80MHz | 12.5mA | 38mA | 46mW | 117mW | 8.6mJ | 13mJ
40MHz | 7.5mA | 20mA | 27mW | 58mW | 10.5mJ | 13mJ
16MHz | 5.5mA | 10mA | 18mW | 39mW | 17.55mJ | 9.9mJ

## Slide 37: Overview
Dataset introduction, challenges
Model selection
Metrics evaluation
Power evaluation
Demo

## Slide 38: Demo!
Tensorflow lite (post train quant) with 8-bit weight quantization on STM32F723
NNoM with CMSIS-NN backend on STM32L475
GUI to automate the process
Real time power figures with APM! (Arduino Power Monitor :)
Actually it has been running for the whole presentation ;)

## Slide 39: Video Demo

## Slide 40: References
[1] https://www.ini.rub.de/upload/file/1470692848_f03494010c16c36bab9e/StallkampEtAl_GTSRB_IJCNN2011.pdf
[2] https://arxiv.org/pdf/1409.4842.pdf
[3] https://arxiv.org/ftp/arxiv/papers/1312/1312.5402.pdf
[4] https://docs.opencv.org/3.4/d3/dc1/tutorial_basic_linear_transform.html
[5] http://yann.lecun.com/exdb/publis/pdf/sermanet-ijcnn-11.pdf
[6] https://gcc.gnu.org/onlinedocs/gcc/Half-Precision.html

## Slide 41: Presentation is finished!
Thank you for you attention!